Tranquillizing rifle Atomvet A13

Operating Manual

Before handling this tranquillizing rifle, read this manual carefully and pay attention to the following safety instructions.

Improper and careless use of the rifle could result in an unintentional gunshot which could cause an injury, death or property damage. Arbitrary adjustments, corrosion and a use of non-standard or damaged projectiles could have the same consequences. In these cases, the manufacturer is not responsible for the consequences.

Before leaving the factory the rifle was tested, carefully inspected and packed.

Atomvet s.r.o. cannot control the use of the rifle after leaving the factory. Therefore, when buying this rifle, make sure it is unloaded and undamaged.

This operating manual should always be stored with the rifle even if it is lent or sold.

SAFETY INSTRUCTIONS

Always follow the safety instructions for your safety and the safety of the others.

1. Always handle your rifle as if it was loaded.

2. Never point your rifle at anything you do not want to shoot.

3. Do not trust anybody that the gun is not loaded.

4. Before putting the rifle down or passing it to another person always make sure that the gun is not loaded.

5. Keep the rifle unloaded with the striking mechanism.

6. Never use the rifle for another purpose than shooting.

7. Never leave the gun loaded and unattended.

8. Before loading the rifle make sure that a barrel bore, chamber and a breech are clean without any obstacles.

9. Before and during shooting do not drink any alcoholic beverages and do not take drugs.

10. Never push a trigger or put your fingers in a trigger guard until you are ready to shoot.

11. Before pushing the trigger check your target once more and the area behind it. The tranquillizing dart can fly behind or through the target several tens of meters.

12. Never shoot at a hard surface such as stone or water surface.

13. If you hold the gun, never make stupid jokes.

14. Before cleaning, storing and transporting your rifle make sure the gun is not loaded.

15. Store the rifle and tranquillizing darts in separate and locked places out of reach and sight of children and unauthorized people.

16. Do not modify any parts of the rifle. It could damage its function and safety.

17. Remember that corrosion, use of damaged darts, dropping the rifle on a hard surface or another bad treatment could cause a serious damage which does not have to be visible at the first sight. If something like this happens, contact the manufacturer and allow the gun to check.

The manufacturer is not responsible for any damages caused by unauthorized manipulation. Safety rules must be observed in any case!

MAINTANANCE INSTRUCTIONS

Disassembly for cleaning

DURING DISASSEMBLY KEEP THE GUN POINTING IN A SAFE DIRECTION!

WARNING!

Do not assembly particular components because they have been set in a factory and unauthorized adjustment can cause change or damage to the setting.

Cleaning of the rifle

The rifle should be cleaned

- after getting wet

- at least once a year in a temperate climate

- at least once a month in difficult weather conditions

-  with a special cloth (with oil for weapons)

Cleaning of the other parts of the rifle

The other parts should be cleaned with a dry soft cloth. You can use a proper polishing agent for the rifle butt.

Waste handling

Materials and product packaging (when used correctly) do not have a negative impact on a human health or the environment. In case of disposing the product or its packaging, metal parts (steel and other metals), plastics, wood, paper and cardboard have to be disposed separately in different collecting containers.

TECHNICAL DATA

| Type | Atomvet A13 |
| --- | --- |
| Calibre [mm] | 11 and 13 mm |
| Total length [mm] | 890 mm |
| Height (without sights) [mm] | 190mm |
| Total width [mm] | 60mm |
| Barrel length [mm] | 850 mm |
| Total weight [kg] | 3900g |
| Filling pressure [bar] | 28bar |
| Muzzle energy [Joule] | 14J |

- Package content:

1x rifle Atomvet A13

1x transport case

5x tranquillizing dart Pneudart 3ml

1x operating manual, ogligatory paperwork

- Pressurization

The pressure required to fire the rifle is made by integrated pump placed directly under the barrel.

- Safety lock

A safety lock locks and unlocks the rifle. It is placed in the middle of the rifle directly above the trigger. A white sign means unlocked, a red sign means locked.

- Pressure regulation

Use the setting wheel above the safety lock to release an excess pressure in the rifle. If you need to re-pressurize, use the integrated pump again.

- Pressure gauge

Pressure gauge helps you to determine the exact pressure in the rifle and how far it can shoot. The more it is pressurized, the further it shoots. If you want to release some pressure, use the setting wheel and release the pressure. When pressurizing to the first red box the rifle shoots up to 20 metres. Green field means shooting for the distance 20 – 30 metres, back red field 40 – 50 metres.

- Removable barrel

The rifle contains two barrels – 11 and 13 mm for different types of tranquillizing darts. A removable barrel is inserted into the outer wider barrel. Loosen the thread at the end of the barrel and pull the removable barrel.

- Bayonet closure

Pull a bayonet closure at the end of the rifle and insert the tranquillizing dart. Use the tip of the closure and insert the dart shot into the barrel. Secure the closure enough to protect it against backward air shot (recoil) or dart shot out of the barrel.